## Slide 1
Lab Update — Paper Recreation 1
Fawaz Mallick · Geyer Lab · May 2026
Where We Are
✓
Recreated pipeline
Full offline recreation of Chen et al. 2021 — feature extraction, quadratic Ridge regression models, sequential Bayesian update (Eq. 1–5).
✓
Treadmill data
Switched from overground to Camargo GTech treadmill data. 8 subjects, 7 trials each (0.5–0.8 m/s). Implemented treadmill velocity compensation in coordinate frame.
✓
Validated
Cross-velocity test (n=5,638): RMSE x = 8.21 cm. Cross-subject AB13 test (n=1,320): RMSE x = 8.81 cm. Competitive with paper's Table II (10.32 cm).
Note on y RMSE: treadmill walking has minimal lateral variability so y is trivially easy. x RMSE is the honest headline number.

## Slide 2
Next Steps
1
IMU-Driven Position Measurement
→ Integrate IMU accelerations from toe-off → heel strike to get a noisy position estimate z = (x̂, ŷ)
→ Accumulated drift gives a natural covariance Σpp — wider for longer strides, noisier sensors
→ Feed P(z | C=(xᵢ,yᵢ)) into Eq. 3 as one additional sequential update on top of the 6 features
→ No new algorithm needed — same framework, same sensor already used for features
2
Feature Relevance Along Z Axis
→ Current features (fA–fF) are computed from AP and ML projections — how much does the Z (vertical) trajectory contribute?
→ Check correlation: scatter fA–fF against xg/yg with Z-axis features overlaid
→ Test whether adding a Z-axis feature (e.g. peak height timing, vertical velocity extremum) reduces γ
→ If Z adds signal → expand feature set and retrain
3
Explore Alternative Features
→ Paper's fA–fF are hand-designed extrema — are there better discriminative features?
→ Candidates: step duration, toe-off angle, mid-swing AP velocity profile shape, pelvis displacement
→ Approach: compute candidate features, check correlation with xg/yg, compare γ before/after
→ Goal: lower γ on harder gait conditions (irregular, variable speed) where current features are weakest