## Slide 1
PROGRESS
UPDATE
Paper Recreation 1
Bayesian Foot Placement Prediction
Chen et al. 2021 — Recreation & Extension
Fawaz Mallick | Course 16-745 | May 2026
Recreated
Bayesian foot placement pipeline from Chen et al. 2021
Validated
Cross-velocity & cross-subject on Camargo treadmill data
Extended
Kalman filter fusion as an additional measurement model

## Slide 2
What Are We Predicting?
Goal
Predict where the foot will land during the early swing phase — before heel strike — so a prosthetic or assistive device can proactively adjust rather than react.
Why Early Prediction?
Reactive control after heel strike is too late for smooth gait. Predicting during swing gives the controller ~300–500 ms of lead time.
Connection to Optimal Control
Foot placement prediction feeds into a cost function that minimizes deviation from desired gait. Predicted (x̂, ŷ) becomes the reference state for the controller.
1
Heel Strike
Stance begins
2
Toe Off
Swing begins
→ prediction window opens
3
Early Swing
Features fA–fF extracted
→ Bayesian update
4
~50% Swing
Prediction output
→ feed to controller
5
Heel Strike
Ground truth
→ error computed

## Slide 3
The Algorithm — Chen et al. 2021
Sequential Bayesian update over a 2D spatial grid. Six swing-phase features update a probability distribution over candidate foot placements.
Eq. 1 — Prior
P₀(C=(xᵢ,yᵢ)) = α₀·(1 + β·Gaussian(cell, (xₕ,yₕ), σ))
Biased toward the average of the previous two strides. We use a uniform prior (no history assumed).
Eq. 2 — Normalization
α₀ = 1 / Σ P₀
Normalizes so probabilities sum to 1 across all ~4000 grid cells.
Eq. 3 — Bayesian Update
Pₙ = αₙ · P(fₙ,ₘ | C=(xᵢ,yᵢ)) · Pₙ₋₁
Multiply current posterior by new feature likelihood, renormalize. Repeated 6 times (one per feature).
Eq. 4 — Likelihood (1D Gaussian)
P(fⱼ,ₘ | C=(xᵢ,yᵢ)) = 1/√(2πγⱼ) · exp(-(fⱼ,ₘ - fⱼ,ₑ(xᵢ,yᵢ))² / 2γⱼ²)
γⱼ = RMSE of the quadratic fit. fⱼ,ₑ = expected feature value at grid cell (xᵢ,yᵢ).
Eq. 5 — Prediction
(x̂, ŷ) = Σ (xᵢ,yᵢ) · P_N(C=(xᵢ,yᵢ) | f₁,ₘ...f₆,ₘ)
Weighted center of mass of the final posterior distribution.

## Slide 4
Dataset & Feature Extraction
Camargo GTech Treadmill Dataset
8 subjects:
AB06 – AB13
7 trials each:
0.50 – 0.80 m/s (0.05 m/s increments)
200 Hz:
Motion capture markers
11,745 steps:
Total extracted (train + test)
Coordinate frame:
Rebuilt every toe-off from last 2 heel-strikes
Treadmill Compensation
Belt velocity added back to AP displacement during swing: l_ap += belt_speed × t. Walking direction fixed via velocity-compensated heel-strike vectors.
6 Swing-Phase Features
fA
First extremum of AP velocity (vₓ)
fB
First positive peak of ML velocity (vᵧ)
fC
First positive peak of vertical velocity (v_z)
fD
Peak heel clearance height
fE
AP displacement at peak height
fF
ML displacement at peak height

## Slide 5
Evaluation Setup
Matching the two-test protocol from Chen et al. 2021 Table II — cross-velocity and cross-subject.
Test 1 — Cross-Velocity
Train subjects:
AB06 – AB12
Train trials:
01, 04, 07 (~0.50, 0.65, 0.80 m/s)
Train steps:
10,425
Test subjects:
AB06 – AB12 (same)
Test trials:
02, 03, 05, 06 (unseen speeds)
Test steps:
5,638
Test 2 — Cross-Subject
Train subjects:
AB06 – AB12
Train trials:
01, 04, 07 (same as Test 1)
Train steps:
10,425
Test subject:
AB13 (fully held out)
Test trials:
All 7 trials
Test steps:
1,320
Grid: AP 0 – 1.4 m × ML ±1.0 m at 2 cm resolution (~4000 cells) · Prior: Gaussian biased toward mean of previous 2 strides

## Slide 6
Results
Both tests use the same trained model. Errors reported in cm.
Test 1 — Cross-Velocity (n = 5,638)
8.21 cm
RMSE x (stride length)
2.81 cm
RMSE y (stride width)
8.68 cm
RMSE distance
Test 2 — Cross-Subject (n = 1,320)
8.81 cm
RMSE x (AB13)
4.34 cm
RMSE y (AB13)
9.82 cm
RMSE distance
17.3 cm
E95 — 95th percentile
distance error (AB13)
8.59 cm
Mean distance error
(AB13)
Note on y RMSE
The paper's subjects walked with intentionally irregular gaits (cross-step, split-step, jog). The Camargo dataset is normal steady-state treadmill walking with minimal lateral variability — so y prediction is naturally easier. x RMSE (8.21 cm) is a genuine result and improves on the paper's 10.32 cm.

## Slide 7
Comparison to Chen et al. 2021
Paper Test 1
(cross-vel)
Ours Test 1
(cross-vel)
Paper Test 2
(cross-sub)
Ours Test 2
(cross-sub)
RMSE x
10.32 cm
8.21 cm
13.00 cm
8.81 cm
RMSE y
8.85 cm
2.81 cm
12.39 cm
4.34 cm
Training steps
~4–5k
10,425
~4–5k
10,425
Gait type
Irregular
Normal TM
Irregular
Normal TM
Data source
IMU
Mocap
IMU
Mocap
Key Differences
More training data
10,425 vs ~4–5k steps → better quadratic fits → lower γ → sharper likelihoods
Easier y task
Normal walking has low lateral variability; the paper's irregular gaits stressed y prediction
Mocap vs IMU
We use ground-truth marker positions, avoiding IMU drift — cleaner features

## Slide 8
Extension — Kalman Filter Fusion
Idea
Use a Kalman filter to track foot position/velocity during swing and fuse its heel-strike prediction with the Bayesian posterior as an additional measurement model (from notes, page 11):
P(c | f₁..f₆, z) ∝ P(z|c) · P_Bayesian(c)
Kalman State X = [x, y, vₓ, vᵧ]
Motion model:
Constant velocity between samples
Process noise Q:
σ_accel² from XSENS MTi-1s spec: 0.002 m/s²/√Hz
Measurement:
Position from synthetic noisy markers
Fusion:
Kalman 2D Gaussian × Bayesian posterior → renormalize
Results
Bayesian only (Test 1)
RMSE x = 8.21 cm RMSE y = 2.81 cm
+ Kalman fusion
RMSE x = 21.38 cm RMSE y = 2.26 cm
Diagnosis
• Kalman initialized with zero velocity at toe-off — wrong on treadmill (foot already has forward velocity from belt)
• Systematic bias: mean error x = −11.1 cm — Kalman pulls predictions shorter
• Step matching achieves 100% (not a data issue)
• Root cause: initial state + treadmill kinematics are incompatible with constant-velocity motion model

## Slide 9
Where This Goes Next
10 days remaining — three concrete directions
01
Fix Kalman Extension
→ Initialize velocity from first 2 swing samples (not zero)
→ Switch to a more appropriate motion model for treadmill kinematics
→ Compare Bayesian-only vs Kalman-fused RMSE
02
Irregular Gait Validation
→ Source or generate perturbed gait data (cross-steps, split-steps)
→ Test whether y RMSE rises to match the paper — confirms the method is sound
→ Documents dataset limitation honestly
03
Optimal Control Connection
→ Formalize how predicted (x̂, ŷ) feeds into the cost function
→ Show how prediction uncertainty (Σpp) propagates into control effort
→ Frame as stochastic MPC: min E[l(xₖ, uₖ)] over predicted foot placements
Fawaz Mallick · Course 16-745 · May 2026